## Slide 1
OSI Model
Open Systems Interconnection — How Data Travels Across a Network
7 Layers
Protocols
Real Examples
Wireshark
Mnemonic: All People Seem To Need Data Processing (Layer 7 down to Layer 1)
See every OSI layer LIVE using Wireshark!

## Slide 2
OSI Model — Why Should You Learn This?
🌐
A Universal Language
IT professionals worldwide use the OSI model as a shared language. When someone says 'Layer 3 problem' — every engineer immediately knows what it means. Switch issue? Layer 2. IP not routing? Layer 3. This common framework works across companies, countries, and technologies.
🔍
A Troubleshooting Framework
When your network breaks, you don't randomly restart things. Start at Layer 1 — is the cable plugged in? Is the signal strong? Work your way up layer by layer until you find where the problem is. This is how professionals debug networks systematically.
📡
Protocol Organization
Every protocol maps to a specific OSI layer. HTTP = Layer 7, TLS = Layer 6, TCP = Layer 4, IP = Layer 3, Ethernet = Layer 2, Cables = Layer 1. Once you understand this mapping, every networking concept starts clicking into place.
OSI = Open Systems Interconnection | Developed by ISO in 1984

## Slide 3
7 Layers at a Glance
All People Seem To Need Data Processing
7
Application
HTTP, FTP, DNS, SMTP
All
L7 Firewall
6
Presentation
SSL/TLS, JPEG, MP4, ASCII
People
—
5
Session
NetBIOS, RPC, PPTP
Seem
—
4
Transport
TCP, UDP, Port Numbers
To
—
3
Network
IP, ICMP, ARP, BGP
Need
Router
2
Data Link
Ethernet 802.3, Wi-Fi 802.11
Data
Switch, AP
1
Physical
Cables, Hubs, Bits, Signals
Processing
Hub, NIC

## Slide 4
Layer 7 — Application Layer
"All"
What does this layer do?
The Application Layer is the interface between the user and the network. When you open a browser and type a URL, send an email, or transfer a file — the Application Layer is at work. It provides network services directly to end-user applications and prepares data for transmission.
Protocols & Technologies
HTTP (Port 80) — Loading websites in your browser
HTTPS (Port 443) — Secure, encrypted websites
FTP (Port 21) — File transfer between systems
DNS (Port 53) — Translating domain names to IP addresses
SMTP (Port 25) — Sending emails
SSH (Port 22) — Secure remote server access
Telnet (Port 23) — Remote access (unencrypted, outdated)
Network Device
Layer 7 Firewall — Performs Deep Packet Inspection on application data
Real World Example
You type google.com in Chrome. The browser builds an HTTP GET request — this happens at Layer 7. The request then travels down through each lower layer before hitting the network.
Wireshark Filter
In Wireshark: type 'http' or 'dns' in the filter bar. You will see all HTTP requests and DNS queries with full headers, URLs, and status codes.
Remember: User interacts directly = Layer 7. Key ports: 80, 443, 21, 22, 25, 53
Layer 7: Application | OSI Model

## Slide 5
Layer 6 — Presentation Layer
"People"
What does this layer do?
The Presentation Layer acts as a translator. It ensures data is in a format the receiving application can understand. It handles three key tasks: data format translation (e.g. JPEG to PNG), encryption and decryption (SSL/TLS), and compression to reduce the size of data before transmission.
Protocols & Technologies
SSL/TLS — Encrypts data for HTTPS connections
JPEG, PNG, GIF — Standard image formats
MP4, H.264 — Video compression standards
ASCII, Unicode — Text encoding standards
EBCDIC — Text encoding for IBM mainframe systems
MIME — Encoding for email attachments
Network Device
No dedicated hardware — Handled by software, OS, and applications
Real World Example
When you log into your bank website over HTTPS, TLS encryption happens at Layer 6. Your password is encrypted here before it ever leaves your device. The server decrypts it at Layer 6 on their end.
Wireshark Filter
In Wireshark: type 'tls' in the filter bar. Watch the TLS handshake — Client Hello, Server Hello, Certificate exchange — this is Layer 6 encryption being set up in real time.
Remember: Encryption, compression, or data format conversion = Layer 6. TLS/SSL = Layer 6.
Layer 6: Presentation | OSI Model

## Slide 6
Layer 5 — Session Layer
"Seem"
What does this layer do?
The Session Layer manages conversations between two devices. It is responsible for establishing a session, maintaining it while data is being exchanged, and terminating it gracefully when the communication ends. If a connection drops mid-session, Layer 5 can attempt to resume it.
Protocols & Technologies
NetBIOS — Session management for Windows networks
RPC (Remote Procedure Call) — Execute code on a remote computer
SIP — Setup and teardown of voice and video calls (VoIP)
PPTP — VPN tunneling protocol
H.245 — Multimedia conference call control
NFS — Network File System session management
Network Device
No dedicated hardware — Managed by application-layer software and the OS
Real World Example
When you make a Zoom call: the call starting is session establishment, staying connected while you talk is session maintenance, and hanging up is session termination. That entire lifecycle is Layer 5.
Wireshark Filter
In Wireshark: type 'sip' in the filter bar. You will see SIP INVITE, 200 OK, and BYE messages — these are the session setup and teardown messages for a VoIP call.
Remember: Connection start, maintain, or end = Layer 5. Video calls, RPC, VoIP = Layer 5.
Layer 5: Session | OSI Model

## Slide 7
Layer 4 — Transport Layer
"To"
What does this layer do?
The Transport Layer delivers data end-to-end between source and destination. It segments large data into smaller chunks, sends them, and reassembles them in the correct order at the destination. The two core protocols are TCP (reliable) and UDP (fast). Port numbers also live at this layer.
Protocols & Technologies
TCP — Reliable, connection-oriented, uses acknowledgements
UDP — Fast, connectionless, no delivery guarantee
Port Numbers — 0-1023 well-known, 1024-49151 registered
TCP 3-Way Handshake — SYN, SYN-ACK, ACK
Flow Control — Manages the speed of data transmission
Error Detection — Checksum to detect corrupted data
Segmentation — Splits large data into smaller segments
Network Device
No hardware device — Handled by the OS networking stack
Real World Example
Downloading a file uses TCP — every packet is acknowledged, and lost packets are resent. YouTube streaming uses UDP — if a frame is lost, the video just keeps playing. Speed matters more than perfection for streaming.
Wireshark Filter
In Wireshark: type 'tcp' and find the 3-way handshake — SYN, SYN-ACK, ACK. Type 'udp' to see UDP traffic. Port numbers are visible in every packet.
Remember: TCP vs UDP = Layer 4. Port numbers = Layer 4. Segmentation = Layer 4.
Layer 4: Transport | OSI Model

## Slide 8
Layer 3 — Network Layer
"Need"
What does this layer do?
The Network Layer routes data from one network to another using IP addresses. Routers operate at this layer. Each router only knows the next hop — but by passing the packet from router to router, data can travel from your laptop in one country to a server on the other side of the world.
Protocols & Technologies
IPv4 — 32-bit addresses (e.g. 192.168.1.1)
IPv6 — 128-bit addresses (future-proof, e.g. 2001:db8::1)
ICMP — Error messages and the ping utility
ARP — Maps IP addresses to MAC addresses
OSPF, BGP, RIP — Routing protocols for path selection
NAT — Translates private IPs to public IPs
TTL — Time To Live, prevents infinite routing loops
Network Device
Router — the Layer 3 device. Layer 3 Switches also possible.
Real World Example
Run 'ping google.com' in your terminal. An ICMP packet travels at Layer 3 from your router to your ISP to Google — each hop checking the destination IP. Run 'traceroute google.com' to see every router along the path.
Wireshark Filter
In Wireshark: type 'icmp' to see ping packets. Type 'ip.addr == 8.8.8.8' to filter traffic to/from Google DNS. See source IP, destination IP, and TTL in every packet.
Remember: IP address = Layer 3. Router = Layer 3 device. ping uses ICMP = Layer 3.
Layer 3: Network | OSI Model

## Slide 9
Layer 2 — Data Link Layer
"Data"
What does this layer do?
The Data Link Layer handles communication within a single network using MAC addresses. While Layer 3 routes between networks, Layer 2 delivers frames within the same LAN. Switches operate here — they maintain a MAC address table and send frames only to the correct destination port.
Protocols & Technologies
Ethernet (IEEE 802.3) — The standard for wired LAN
Wi-Fi (IEEE 802.11) — The standard for wireless LAN
MAC Addresses — 48-bit hardware addresses (e.g. AA:BB:CC:DD:EE:FF)
ARP — Resolves IP addresses to MAC addresses
PPP — Point-to-Point Protocol for direct connections
VLAN (802.1Q) — Virtual LANs on shared physical infrastructure
STP — Spanning Tree Protocol, prevents switching loops
Network Device
Switch (Layer 2) — forwards frames by MAC address. Access Point (Layer 2 bridge).
Real World Example
Your laptop sends a packet to the switch. The switch checks its MAC address table and sends the frame only to the correct port — just to the destination device, not broadcast to everyone. That selective forwarding is Layer 2.
Wireshark Filter
In Wireshark: type 'eth' to see Ethernet frames with source and destination MAC addresses. Type 'arp' to see ARP requests — your device asking 'Who has this IP address? Tell me your MAC!'
Remember: MAC address = Layer 2. Switch = Layer 2. Ethernet/Wi-Fi = Layer 2. Frame = L2 PDU.
Layer 2: Data Link | OSI Model

## Slide 10
Layer 1 — Physical Layer
"Processing"
What does this layer do?
The Physical Layer is the actual physical medium — copper cables, fiber optic cables, or wireless radio signals. At this layer there is no addressing, no error correction, and no protocols. Just raw bits — zeros and ones — converted into electrical signals, pulses of light, or radio waves and sent across the medium.
Protocols & Technologies
Ethernet cables — Cat5e (up to 1 Gbps), Cat6 (up to 10 Gbps)
Fiber Optic — Single mode (long distance), Multi mode (short distance)
Wi-Fi signals — 2.4 GHz, 5 GHz, and 6 GHz frequency bands
Bit rate — Number of bits transmitted per second
Connectors — RJ-45, LC, SC, SFP transceivers
Hubs — Broadcast all signals to every port (Layer 1 device)
NIC — Network Interface Card, sends and receives bits
Network Device
Hub (Layer 1 — broadcasts to all ports). Cables, Repeaters, NICs, Modems.
Real World Example
Your internet is slow. Start troubleshooting at Layer 1 — is the cable damaged or loose? Is your Cat5e cable limiting you to 100Mbps when you need 1Gbps? Is your Wi-Fi signal weak because you are too far from the router? Physical issues are always checked first.
Wireshark Filter
Wireshark starts at Layer 2 — Layer 1 itself is not directly visible. However, frequent CRC errors or malformed frames in Wireshark often indicate an underlying Layer 1 physical problem.
Remember: Cable, signal, NIC, Hub = Layer 1. Physical troubleshooting always starts at Layer 1!
Layer 1: Physical | OSI Model

## Slide 11
Wireshark — See Live Network Traffic on Your Screen
What is Wireshark?
Wireshark is a free, open-source network protocol analyzer. It captures every packet passing through your network interface and lets you inspect it in detail. You can see OSI layers 2 through 7 in real time — watching data actually travel across the network.
Installation — Step by Step
1. Go to wireshark.org and click Download
2. Download the Windows Installer (.exe)
3. During install — make sure to install Npcap or WinPcap (required for packet capture)
4. On Kali Linux: sudo apt install wireshark
5. On Kali: sudo usermod -aG wireshark $USER (then log out and back in)
Wireshark: 3 Panels
Panel 1 — Packet List
Top section: Every captured packet as a row. Shows time, source IP, destination IP, protocol, and info.
Panel 2 — Packet Details
Middle section: The selected packet broken down layer by layer. Expand each layer to see OSI in action.
Panel 3 — Packet Bytes
Bottom section: Raw hex and ASCII bytes — the actual data that traveled across the cable.
Download: wireshark.org
Wireshark — Free & Open Source Network Analyzer | wireshark.org

## Slide 12
Wireshark — See Each OSI Layer Live
Start capturing: Select your interface (Wi-Fi or eth0) → Click the green Shark button → Traffic will start flooding in immediately
Layer 7
http
Website traffic — see HTTP requests and responses, GET/POST methods, URLs, status codes like 200 OK or 404 Not Found
Layer 7
dns
DNS queries — see which domain resolved to which IP address. Both the question and answer are shown
Layer 6
tls
TLS handshake — the encryption setup process. Client Hello, Server Hello, Certificate, Finished
Layer 4
tcp
TCP connections — find the 3-way handshake (SYN, SYN-ACK, ACK). Port numbers clearly visible on every packet
Layer 4
udp
UDP packets — connectionless and fast. DNS, DHCP, video streaming all use UDP
Layer 3
icmp
Ping traffic — ICMP Echo Request and Echo Reply. TTL and IP headers clearly visible
Layer 3
ip.addr == 8.8.8.8
Filter only traffic to/from Google DNS. Replace 8.8.8.8 with any IP address to isolate specific traffic
Layer 2
arp
ARP requests — your device broadcasting to find the MAC address for a given IP. Network discovery in action
Type any filter in the Wireshark filter bar and press Enter — live traffic filtered instantly

## Slide 13
Wireshark — Practical Exercise: Trace Every OSI Layer
Exercise: Capture a real HTTP request and identify every OSI layer inside a single packet
1
Start Capturing
Open Wireshark → Select your interface (Wi-Fi or eth0) → Click the green button → Capture starts
2
Open http://example.com in Browser
Use HTTP (not HTTPS) so we can see unencrypted data. Type the URL and press Enter
3
Filter: http
Type "http" in the Wireshark filter bar. Find the HTTP GET request row and click on it
4
Expand the Packet Details Panel
In the middle panel, expand each section — Frame → Ethernet → IP → TCP → HTTP (every OSI layer!)
5
Note What Each Layer Shows
L1: Frame bytes | L2: MAC addresses | L3: IP src/dst | L4: TCP ports | L7: HTTP GET /
6
Follow TCP Stream
Right-click the packet → Follow → TCP Stream. See the full conversation — your request and the server response
After this exercise, the OSI model will make complete sense — you will see it working live!

## Slide 14
Data Encapsulation — What Each Layer Adds
When sending data: Top to bottom — each layer adds its own header (Encapsulation). When receiving: Bottom to top — each layer reads and removes its header (De-encapsulation).
L7 — Data
+ HTTP headers, application data
L6 — Data
+ Encryption / format conversion (TLS)
L5 — Data
+ Session tokens, connection identifiers
L4 — Segment
+ TCP/UDP header: src port, dst port, seq#
L3 — Packet
+ IP header: source IP, destination IP, TTL
L2 — Frame
+ Ethernet header: src MAC, dst MAC + FCS
L1 — Bits
+ Physical signal: electrical / light / radio
Header Added →
PDU Names: L7-L5 = Data | L4 = Segment | L3 = Packet | L2 = Frame | L1 = Bits

## Slide 15
Quick Reference — Complete Revision Card
Layer
Name
Protocols
Device
Mnemonic
Wireshark
7
Application
HTTP/HTTPS, FTP, DNS, SMTP, SSH
L7 Firewall
All
http, dns
6
Presentation
SSL/TLS, JPEG, MP4, ASCII
—
People
tls, ssl
5
Session
NetBIOS, RPC, SIP, NFS
—
Seem
sip
4
Transport
TCP, UDP, Port Numbers
—
To
tcp, udp
3
Network
IP, ICMP, ARP, BGP
Router
Need
icmp, ip
2
Data Link
Ethernet 802.3, Wi-Fi 802.11, MAC
Switch, AP
Data
arp, eth
1
Physical
Cables, Hubs, NIC, Bits, Signals
Hub, NIC
Processing
—
All People Seem To Need Data Processing — (Layer 7 down to Layer 1)

## Slide 16
Summary
Key Takeaways — OSI Model
The OSI Model has 7 layers — from Layer 1 (Physical) up to Layer 7 (Application)
Mnemonic: All People Seem To Need Data Processing — Layer 7 down to Layer 1
Router = Layer 3 | Switch = Layer 2 | Hub = Layer 1
TCP/UDP = Layer 4 | IP address = Layer 3 | MAC address = Layer 2
Use Wireshark to see every layer live — best way to truly understand networking
When troubleshooting — always start at Layer 1 and work your way up
Next Topic: Networking Devices — Switches, Routers, Firewalls, Access Points →